## Slide 1
M.Tech Program
Advanced Industry Integrated Programs
Jointly offered by University and LTIMindTree
Project Title 1:
AeroHydro-PINN Multimodal Physics-AI for Wake-Aware Hydrogen Optimization
S.Swetha
VIT CHENNAI
Knowledge partner | Implementation partner

## Slide 2
Wind farms lose 10–40% of downstream turbine power to wake effects, directly reducing electricity available for green hydrogen electrolysis.
Traditional CFD simulations that model this accurately take days to weeks, making real-time optimization impractical.
AeroHydro-PINN solves this using a Physics-Informed Neural Network (PINN) — a model trained with real fluid-momentum physics built into its loss function
Delivering CFD-quality wake awareness at millisecond inference speed, then feeding the result into a real electrolyzer model to estimate hydrogen yield.
Introduction
Project Title - Calibri body 18

## Slide 3
Design and deploy an end-to-end pipeline that predicts wind turbine wake deficit and resulting hydrogen production in real-time, enabling operational optimization without relying on expensive CFD.
Generate a physically valid wake dataset using a validated wake model (Bastankhah-Gaussian, via PyWake).To Train a PINN constrained by actuator-disk momentum conservation.
Model hydrogen output using real PEM electrolyzer electrochemistry. Build an optimizer recommending turbine/electrolyzer spacing for max yield. Deploy as a containerized, cloud-hosted API.
Objectives
Project Title - Calibri body 18

## Slide 4
Wind-turbine-to-turbine wake modelling and its downstream impact on electrolytic hydrogen production; a PINN trained on analytical wake-model output, validated conceptually against real SCADA data trends (Kelmarsh, Penmanshiel); a physics-based hydrogen production model; a REST API and optimization endpoint.
Full 3D CFD simulation (requires HPC infrastructure and weeks of compute — exactly the bottleneck this project avoids); ship-hull hydrodynamic wake CFD (no free dataset exists at that fidelity; would require a separate multi-month naval CFD campaign); real-time SCADA integration with a live wind farm (requires operational access this project doesn't have).
Scope
Project Title - Calibri body 18

## Slide 5
Jensen (1983) introduced the first analytical wake model; Bastankhah & Porté-Agel (2014) improved it with a Gaussian deficit profile now used industry-wide (PyWake, FLORIS). Raissi et al. (2019) introduced Physics-Informed Neural Networks; Eivazi et al. (2022) applied PINNs to turbulent wake flows with CFD-comparable accuracy.
Sanchez et al. (2020) published the PEM electrolyzer polarization curve used in NREL's H2A model; IRENA (2020) confirms wake losses materially affect green hydrogen cost. Gap: no public project combines a PINN wake surrogate with a physics-grounded hydrogen model in one deployable, real-time pipeline.
Literature Review
Project Title - Calibri body 18

## Slide 6
Summary of Literature
Project Title - Calibri body 18
Source | Contribution | Relevance
Jensen (1983) | First analytical wake model | Historical baseline
Bastankhah & Porté-Agel (2014) | Gaussian wake deficit model | Used via PyWake for training data
Raissi et al. (2019) | Introduced PINNs | Core methodology
Eivazi et al. (2022) | PINNs on turbulent wakes | Validates approach feasibility
Sanchez et al. (2020) | PEM electrolyzer polarization curve | Used in hydrogen module
IRENA (2020) | Green hydrogen cost economics | Motivates wake-aware optimization

## Slide 7
A plain neural network can violate real physics in sparsely-sampled regions (e.g., predicting deficit that increases with distance); the physics-residual loss in this project prevents that.
PyWake's wake models are peer-reviewed and validated against real SCADA data by DTU Wind Energy — the same class of model used in commercial wind farm assessments. The full pipeline trains and runs in under 15 minutes on a standard CPU, needing no GPU or cloud credits.
Additional Information…. Calibri body -36
Project Title - Calibri body 18

## Slide 8
Module 1 : Wake Physics Data Generation
Simulates realistic wake behavior across the Horns Rev 1 wind farm using PyWake, producing the labeled training data for the PINN.
1.1 Site & turbine setup: Horns Rev 1 layout + V80 turbine specs (real, published).
1.2 Wind sweep design: 72 directions × 15 speeds = 1,080 scenarios.
1.3 Wake computation: Bastankhah-Gaussian model run per turbine per scenario.
1.4 Dataset export: CSV with position, wind condition, deficit, power, turbulence
Modules
Project Title - Calibri body 18

## Slide 9
2. Module 2: Physics-Informed Neural Network
Learns wake deficit from data while respecting real momentum-conservation physics.
2.1 Architecture: 4-layer fully-connected network, Tanh activations.
2.2 Data loss: Supervised MSE against PyWake output.
2.3 Physics loss: Momentum-conservation residual via autograd.
2.4 Training loop: Combined loss, Adam optimizer, validation tracking.
2.5 Checkpointing: Best model saved automatically.
Modules
Project Title - Calibri body 18

## Slide 10
3. Module 3: Hydrogen Production Modelling
Converts predicted turbine power into hydrogen output using real electrochemistry.
3.1 Polarization curve: Published PEM voltage-current equation.
3.2 Current solver: Bisection method finds operating point.
3.3 Faraday's law: Converts current to hydrogen mass flow.
3.4 Stack sizing: Scaled to realistic multi-MW turbine output.
Modules
Project Title - Calibri body 18

## Slide 11
4. Module 4: Optimization Layer
Recommends turbine spacing to maximize hydrogen yield.
4.1 Candidate evaluation: Tests multiple spacing options via the PINN.
4.2 Yield-per-area metric: Normalizes output by spacing used.
4.3 Recommendation: Selects the best-performing configuration.
Module
Project Title - Calibri body 18

## Slide 12
5 .Module 5: Deployment and Service Layer
Makes the pipeline usable as a real, callable service.
5.1 API endpoints: /health, /predict/wake, /optimize/spacing.
5.2 Validation: Pydantic schemas for all requests.
5.3 Containerization: Dockerfile for portable deployment.
5.4 Cloud deployment: Railway configuration included.
5.5 Testing: Postman collection for all endpoints.
Module
Project Title - Calibri body 18

## Slide 13
6 . Module 6: Validation and Evaluation
Confirms accuracy and physical trustworthiness before use.
6.1 Cross-validation: Held-out scenario MSE.
6.2 Physical plausibility: Checks monotonicity and energy conservation.
6.3 Real-data comparison (optional): Trend check against Kelmarsh/Penmanshiel SCADA data.
Module
Project Title - Calibri body 18